## Slide 1
UNIT 1 INTRODUCTION to NUMBER SYSTEMS and CONVERSION
Objectives
Study Guide
1.1 Digital Systems and Switching Circuits
1.2 Number Systems and Conversion
1.3 Binary Arithmetic
1.4 Representation of Negative Numbers
1.5 Binary Codes

## Slide 2
Objectives
Topics introduced in this chapter:
Difference between Analog and Digital System
Difference between Combinational and Sequential Circuits
Binary number and digital systems
Number systems and Conversion
Add, Subtract, Multiply, Divide Positive Binary Numbers
1’s Complement, 2’s Complement for Negative binary number
BCD code, 6-3-1-1 code, excess-3 code

## Slide 3: 1.1 Digital Systems and Switching Circuits
Digital systems: computation, data processing, control,
communication, measurement
- Accuracy, reliability
Analog – continuous
- Natural phenomena
(pressure, temperature, speed…)
- Difficulty in realizing, processing using electronics
Digital – discrete
- Binary digit  signal processing as bit unit
- Easy in realizing, processing using electronics
- High performance due to integrated circuit technology

## Slide 4: Analog (Continuous) vs Digital (Discrete)
0
1
2
23
(time)
(temp.)
continuous
(time)
(temp.)
△ t
comparison
operation
recognition
※ △ t ≠ 0
discrete

## Slide 5: Analog (Continuous) vs Digital (Discrete) Signals
Continuous signal
Digital signal
Discrete sampled signal

## Slide 6: Quantization (Discrete Signal)
․ sampling → quantization
7
8
9
6
(temp.)
(time)
2
3
4
1
(bit)
(time)
(quantization)

## Slide 7
Binary Digit?
Binary:- Two values (0, 1)
- Each digit is called as a “bit”
Number representation with only two values (0,1)
Can be implemented with simple electronics devices
(ex: Voltage: High(1), Low(0)
Switch: On (1), Off(0)…)
Good Things in Binary Number

## Slide 8: Digital Circuit (Switching Circuit)
Combinational Circuit :
  - outputs depend on only present inputs, not on past inputs
Sequential Circuit:
  - outputs depend on both present inputs and past inputs
  - has “memory” function

## Slide 9: 1.2 Number Systems and Conversion
Decimal: 0..9
Binary: 0 and 1
Hexadecimal: 0..9 and A..F
Decimal | Binary | Hexadecimal
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
16 | 10000 | 10
17 | 10001 | 11

## Slide 10: 1.2 Number Systems and Conversion
Decimal: uses digits from 0..9
Binary: uses only 0 and 1
Hexadecimal: uses digits from 0..9 and A..F
Positional Notation

## Slide 11: 1.2 Number Systems and Conversion
Radix(Base):
Example:
Positional Notation

## Slide 12: 1.2 Number Systems and Conversion
Conversion of Decimal to Base-R

## Slide 13: 1.2 Number Systems and Conversion
53
2
26
2
13
2
6
2
3
2
1
2
rem. = 1 = a0
rem. = 0 = a1
rem. = 1 = a2
rem. = 0 = a3
rem. = 1 = a4
0
rem. = 1 = a5
Example: Decimal to Binary Conversion

## Slide 14: 1.2 Number Systems and Conversion
Conversion of a decimal fraction to Base-R
Example:

## Slide 15: 1.2 Number Systems and Conversion
Process starts repeating here because .4 was previously
obtained
Example: Convert 0.7 to binary

## Slide 16: 1.2 Number Systems and Conversion
45
7
6
7
0
rem.6
rem.3
Example: Convert 231.34 to base-7

## Slide 17: 1.2 Number Systems and Conversion
Conversion of Binary to Octal, Hexadecimal
(101011010111 )2 = ( )8, octal
(10111011)2 = ( )8, octal
(1010111100100101)2 = ( )16, Hexadecimal
(1101101000)2 = ( )16, Hexadecimal
.

## Slide 18: 1.3 Binary Arithmetic
Addition
Example:
0 + 0 = 0 | 
0 + 1 = 1 | 
1 + 0 = 1 | 
1 + 1 = 0 | and carry 1 to the next column
 | 1 | 1 | 1 | 1 |  | carries
1310 = |  | 1 | 1 | 0 | 1 | 
1110 = |  | 1 | 0 | 1 | 1 | 
2410 = | 1 | 1 | 0 | 0 | 0 | 

## Slide 19: 1.3 Binary Arithmetic
(indicates
a borrow
from the
3rd column)
borrows
borrows
Subtraction
Example:
0 - 0 = 0 | 
0 - 1 = 1 | and borrow 1 from the next column
1 - 0 = 1 | 
1 - 1 = 0 | 

## Slide 20: 1.3 Binary Arithmetic
column 2
column 1
note borrow from column 1
note borrow from column 2
Subtraction Example with Decimal

## Slide 21: 1.3 Binary Arithmetic
multiplicand
multiplier
first partial product
second partial product
sum of first two partial products
third partial product
sum after adding third partial product
fourth partial product
final product (sum after adding fourth partial prodoct)
Multiplication
Multiply: 13 x11(10)

## Slide 22: 1.3 Binary Arithmetic
The quotient is 1101 with a remainder
of 10.
Division

## Slide 23: 1.4 Representation of Negative Numbers
b
n
1
–
b
1
b
0
Magnitude
MSB
(a) Unsigned number
b
n
1
–
b
1
b
0
Magnitude
Sign
(b) Signed number
b
n
2
–
0 denotes
1 denotes
+
–
MSB

## Slide 24: 1.4 Representation of Negative Numbers
b
n
1
–
b
1
b
0
Magnitude
MSB
(a) Unsigned number
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7

## Slide 25: 1.4 Representation of Negative Numbers
(b) Signed number
b
n
1
–
b
1
b
0
Magnitude
Sign
b
n
2
–
0 denotes
1 denotes
+
–
MSB
000 | 0
001 | 1
010 | 2
011 | 3
100 | -4
101 | -3
110 | -2
111 | -1
2’s Complement

## Slide 26: 1.4 Representation of Negative Numbers
2’s complement representation for negative numbers
+N | Positive integers
+0 | 0000
+1 | 0001
+2 | 0010
+3 | 0011
+4 | 0100
+5 | 0101
+6 | 0110
+7 | 0111
- | -
-N | Negative integers |  | 
 | Sign and magnitude | 2’s complement | 1’s complement
-0 | 1000 | - | 1111
-1 | 1001 | 1111 | 1110
-2 | 1010 | 1110 | 1101
-3 | 1011 | 1101 | 1100
-4 | 1100 | 1100 | 1011
-5 | 1101 | 1011 | 1010
-6 | 1110 | 1010 | 1001
-7 | 1111 | 1001 | 1000
-8 | - | 1000 | -
-N | Negative integers |  | 
 | Sign and magnitude |  | 
-0 | 1000 | - | 1111
-1 | 1001 | 1111 | 1110
-2 | 1010 | 1110 | 1101
-3 | 1011 | 1101 | 1100
-4 | 1100 | 1100 | 1011
-5 | 1101 | 1011 | 1010
-6 | 1110 | 1010 | 1001
-7 | 1111 | 1001 | 1000
-8 | - | 1000 | -

## Slide 27: 1.4 Representation of Negative Numbers
1’s complement representation for the given number
Example: Find the 1’s complement of .

## Slide 28: 1.4 Representation of Negative Numbers
2’s complement representation for the given number
Example: Find the 2’s complement of .
2’s complement = 1’s complement + 1

## Slide 29: 1.4 Representation of Negative Numbers
Given a negative number by its 2’s complement,
 To obtain the magnitude of the integer
Taking 2’s complement of N*
2’s complement representation for the negative numbers

## Slide 30: 1.4 Representation of Negative Number
(correct answer)
wrong answer because of overflow (+1110 requires
5 bits including sign)
(correct answer)
Case 1
Case 2
Case 3
Addition of 2’s complement numbers

## Slide 31: 1.4 Representation of Negative Number
correct answer when the carry from the sign bit
is ignored (this is not an overflow)
Case 4
Addition of 2’s complement numbers
Proof

## Slide 32: 1.4 Representation of Negative Numbers
correct answer when the last carry is ignored
(this is not an overflow)
Case 5
Addition of 2’s complement numbers
Proof

## Slide 33: 1.4 Representation of Negative Numbers
wrong answer because of overflow
(-1110 requires 5 bits including sign)
Case 6
Addition of 2’s complement numbers

## Slide 34: 1.4 Representation of Negative Numbers
(correct answer)
(end-around carry)
(correct answer, no overflow)
(end-around carry)
(correct answer, no overflow)
Case 3
Case 4
Case 5
Addition of 1’s complement numbers

## Slide 35: 1.4 Representation of Negative Numbers
(end-around carry)
(wrong answer because of overflow)
Case 6
Addition of 1’s complement Numbers

## Slide 36: 1.4 Representation of Negative Numbers
(end-around carry)
(end-around carry)
Addition of 1’s complement Numbers
Addition of 2’s complement Numbers

## Slide 37: 1.5 Binary Codes
Decimal Digits | 8-4-2-1 Code (BCD) | Excess-3 Code | Gray Code
0 | 0000 | 0011 | 0000
1 | 0001 | 0100 | 0001
2 | 0010 | 0101 | 0011
3 | 0011 | 0110 | 0010
4 | 0100 | 0111 | 0110
5 | 0101 | 1000 | 1110
6 | 0110 | 1001 | 1010
7 | 0111 | 1010 | 1011
8 | 1000 | 1011 | 1001
9 | 1001 | 1100 | 1000

## Slide 38: 1.5 Binary Codes
1010011 1110100 1100001 1110010 1110100
S t a r t
ASCII (American Standard Code for Information Interchange) Code

## Slide 39
ASCII Code (incomplete)