## Slide 1
UNIT 11 LATCHES AND FLIP-FLOPS
This chapter in the book includes:
Objectives
Study Guide
11.1 Introduction
11.2 Set-Reset Latch
11.3 Gated D Latch
11.4 Edge-Triggered D Flip-Flop
11.5 S-R Flip-Flop
11.6 J-K Flip-Flop
11.7 T Flip-Flop
11.8 Flip-Flop with Additional Inputs
11.9 Summary
Problems

## Slide 2: Objectives
S-R and gated D latches
2. D, D-CE, S-R, J-K and T flip-flops
3. Characteristic (next-state) equations
4. Timing diagram
5. Construction analysis of latches and
flip-flops using gates

## Slide 3: 11.1 Introduction
Logic Circuit
Combinational logic circuit
Sequential logic circuit: output depends on
  Present input
  Past sequence of inputs
    Memory circuit
    Feedback circuit

## Slide 4: 11.1 Introduction
Unstable state
An Inverter with Feedback
Two Inverters with Feedback
Stable state

## Slide 5: 11.2 Set-Reset Latch
S=R=0  Q=0
Simple Latch
Two stable states and has memory function
S=1, R=0  Q=1
S=R=0  Q=1
S=0, R=1  Q=0

## Slide 6: 11.2 Set-Reset Latch
S-R Latch
S: Sets the output to Q=1
R: Resets the output to Q=0
S=R=1 is not allowed
Cross-coupled Form
Symbol

## Slide 7: 11.2 Set-Reset Latch
Improper S-R Latch Operation (S=R=1 is prohibited)
If S=R=1, then
  It violates the basic rule of latch operation
  It oscillates

## Slide 8: 11.2 Set-Reset Latch
Timing Diagram for S-R Latch
ε: response time or delay time

## Slide 9: 11.2 Set-Reset Latch
S-R Latch Operation
S(t) R(t) Q(t) | Q(t+ε)
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 1 0 0 1 1 - -
Inputs not allowed
Q(t): Present state
Q(t+ ε): Next state

## Slide 10: 11.2 Set-Reset Latch
Characteristic Equation for S-R Latch
0
1
0
0
1
1
-
-
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Q(t+ε)
S(t) R(t) Q(t)
0
1

## Slide 11: 11.2 Set-Reset Latch
Switch Debouncing with an S-R Latch
Application of an S-R Latch

## Slide 12: 11.2 Set-Reset Latch
Alternative Form of the S-R Latch Using NAND Gates: Latch
0
1
0
0
1
1
-
-
1 1 0
1 1 1
1 0 0
1 0 1
0 1 0
0 1 1
0 0 0
0 0 1
Q(t+ε)
S(t) R(t) Q(t)

## Slide 13: 11.3 Gated D Latch
Gated D Latch
Transparent Latch

## Slide 14: 11.3 Gated D Latch
Symbol and Truth Table for Gated D Latch
G D Q | Q+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 1 0 1 0 0 1 1

## Slide 15: 11.4 Edge-Triggered D Flip-Flop
Flip-Flop
  Output changes only in response to the clock
Rising-edge (positive-edge) Triggered Flip-Flop
  Output changes in response to a 0 to 1 transition on the clock
Falling-edge (negative-edge) Triggered Flip-Flop
Output changes in response to a 1 to 0 transition on the clock
Active Edge
  Clock edge (rising or falling) that triggers the flip-flop

## Slide 16: 11.4 Edge-Triggered D Flip-Flop
D Flip-Flops
D Q | Q+
0 0 0 1 1 0 1 1 | 0 0 1 1
Truth table
Timing for D Flip-Flop (Falling-Edge Trigger)

## Slide 17: 11.4 Edge-Triggered D Flip-Flop
D Flip-Flop (Rising-Edge Trigger)

## Slide 18: 11.4 Edge-Triggered D Flip-Flop
D Flip-Flop (Rising-Edge Trigger)
Setup and Hold Times for an Edge-Triggered D Flip-Flop

## Slide 19: 11.4 Edge-Triggered D Flip-Flop
Determination of Minimum Clock Period

## Slide 20: 11.5 S-R Flip-Flop
S-R Flip-Flop
Operation Summary
S=R=0 no state change
S=1, R=0 set Q to 1 (after active Ck edge)
S=0, R=1 reset Q to 0 (after active Ck edge)
S=R=1 not allowed

## Slide 21: 11.5 S-R Flip-Flop
S-R Flip-Flop Implementation and Timing (Master-Slave Flip-Flop)

## Slide 22: 11.6 J-K Flip-Flop
J-K Flip-Flop (Rising Edge Trigger Type)
J K Q | Q+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 1 0 0 1 1 1 0
Next state table and characteristic equation

## Slide 23: 11.6 J-K Flip-Flop
J-K Flip-Flop (Timing Chart)
J K Q | Q+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 1 0 0 1 1 1 0

## Slide 24: 11.6 J-K Flip-Flop
Master-Slave J-K Flip-Flop (Rising Edge Trigger Type)

## Slide 25: 11.7 T Flip-Flop
T Flip-Flop
T Q | Q+
0 0 0 1 1 0 1 1 | 0 1 1 0

## Slide 26: 11.7 T Flip-Flop
Timing Diagram for T Flip-Flop (Falling-Edge Trigger)
T Q | Q+
0 0 0 1 1 0 1 1 | 0 1 1 0

## Slide 27: 11.7 T Flip-Flop
Implementation of T Flip-Flop

## Slide 28: 11.8 Flip-Flops with Additional Inputs
D Flip-Flop with Asynchronous Clear and Preset Inputs
Ck D PreN ClrN | Q+
x x 0 0 x x 0 1 x x 1 0 ↑ 0 1 1 ↑ 1 1 1 0,1,↓ x 1 1 | (not allowed) 1 0 0 1 Q(no charge)

## Slide 29: 11.8 Flip-Flops with Additional Inputs
Timing Diagram for D Flip-Flop with Asynchronous Clear and Preset

## Slide 30: 11.8 Flip-Flops with Additional Inputs
D Flip-Flop with Clock Enable
The MUX output :
The characteristic equation :
(may result in loss of synchronization)
(ideal synchronization)

## Slide 31: 11.9 Summary
(S-R latch or flip-flop)
(gated D latch)
(D flip-flop)
(D-CE flip-flop)
(J-K flip-flop)
(T flip-flop)