## Slide 1
UNIT 12 REGISTERS AND COUNTERS
This chapter in the book includes:
Objectives
Study Guide
12.1 Registers and Register Transfers
12.2 Shift Registers
12.3 Design of Binary Counters
12.4 Counters for Other Sequences
12.5 Counter Design Using S-R and J-K Flip-Flops
12.6 Derivation of Flip-Flop Input Equations--Summary
Problems

## Slide 2
Objectives
Explain the operation of registers. Understand how to transfer data
between registers using tri-state bus
2. Explain the shift register operation, how to build them and
analyze operation. Construct a timing diagram for a shift register
3. Explain the operation of binary counters, how to build them using F/F
and gates and analyze operation.
4. Given the present state and desired next state of F/F, determine
the required F/F/ inputs
5. Given the desired counting sequence for a counter, derive F/F input equations.
6. Explain the procedures used for deriving F/F input equation.
7.Construct a timing diagram for a counter by tracing signals through the circuit.

## Slide 3
Registers and Counters
Register
  A group of flip-flops
  Use a common clock input
  Used to store and shift binary data
Counter
  A group of flip-flops
  Change states in a prescribed sequence

## Slide 4
12.1 Registers and Register Transfers
4-Bit D Flip-Flop Registers with Data, Load, Clear, and Clock inputs
Load signal ANDed with Clk signal → may cause timing problems
ClrN signal for asynchronous clear

## Slide 5
12.1 Registers and Register Transfers
4-Bit D Flip-Flop Registers with Data, Load, Clear, and Clock inputs
Load signal is applied to CE (Clock Enable) pin

## Slide 6
12.1 Registers and Register Transfers
4-Bit D Flip-Flop Registers with Data, Load, Clear, and Clock inputs
Symbol
Bus
Bus
4
4
ClrN
CE
Clr
Q
Load
Clk
D

## Slide 7: 12.1 Registers and Register Transfers
Data Transfer Between Registers

## Slide 8: 12.1 Registers and Register Transfers
Data Transfer Between Registers (A → Q)
EN = 1
Load = 1

## Slide 9: 12.1 Registers and Register Transfers
Data Transfer Between Registers (B → Q)
EN = 0
Load = 1

## Slide 10
12.1 Registers and Register Transfers
8-Bit Register with Tri-State Output

## Slide 11
Data Transfer Using a Tri-State Bus
12.1 Registers and Register Transfers
LdH

## Slide 12: 12.1 Registers and Register Transfers
Parallel Adder with Accumulator

## Slide 13: 12.1 Registers and Register Transfers
Typical Adder Cell with Multiplexer

## Slide 14: 12-2 Shift Registers
4-bit Right-Shift Register
01011010110101101011
Shifting occurs when Shift = 1

## Slide 15: 12-2 Shift Registers
4-bit End-Around Right-Shift Register

## Slide 16: 12-2 Shift Registers
8-Bit Serial-in, Serial-out Shift Register ( Commercialized in IC )

## Slide 17: 12-2 Shift Registers
Typical Timing Diagram for Shift Register

## Slide 18: 12-2 Shift Registers
Parallel-in, Parallel-Out Right Shift Register

## Slide 19: 12-2 Shift Registers
Parallel-in, Parallel-Out Right Shift Register
Inputs Sh (Shift) L(Load) | Next State Q3+ Q2+ Q1+ Q0+ | Action
0 0 0 1 1 X | Q3 Q2 Q1 Q0 D3 D2 D1 D0 SI Q3 Q2 Q1 | No change Load Right shift

## Slide 20: 12-2 Shift Registers
The Next-state Equations for the Shifter Register
Typical Application of the Shifter Register
Conversion of parallel data to serial data

## Slide 21: 12-2 Shift Registers
Timing Diagram for Shift Register

## Slide 22: 12-2 Shift Registers
Shift Register with Inverted Feedback  Johnson Counter
A 3-bit shift register
Successive states
Initial states = 000
Initial states = 010

## Slide 23: 12.3 Design of Binary Counters
Counter
Synchronous counter
  State changes occur simultaneously
Asynchronous counter (Ripple counter)
  One flip-flop triggers the next flip-flop in line

## Slide 24: 12.3 Design of Binary Counters
A binary counter using three T F/F to count clock pulses
Design of a 3-bit Synchronous Binary Counter by Inspection of Counting Sequence
C B A
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
…
Counting
Sequence
To determine the flip-flop inputs – TA, TB, TC
A changes state for every clock input
B changes state if A = 1
C changes state if A = 1 and B = 1
→ TC = A AND B
→ TA = 1
→ TB = A

## Slide 25: 12.3 Design of Binary Counters
A binary counter using three T F/F to count clock pulses
TC = A AND B
TA = 1
TB = A
Design of a 3-bit Synchronous Binary Counter by Inspection of Counting Sequence

## Slide 26: 12.3 Design of Binary Counters
State Table for 3-bit Binary Counter
Design of a 3-bit Synchronous Binary Counter by Using a State Table
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ TC TB TA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 1 0 0 1 1 1 1 0 1 0 0 1 1 1 0 0 1 1 1 1 1 0 0 1 0 0 0 1 1 1

## Slide 27: 12.3 Design of Binary Counters
Karnaugh Map for 3-bit Synchronous Binary Counter
TA = 1, TB = A, TC = AB

## Slide 28: 12.3 Design of Binary Counters
3-bit Synchronous Binary Counter with D Flip-Flops
To convert each D flip-flop to a T flip-flop by adding XOR gates

## Slide 29: 12.3 Design of Binary Counters
3-bit Synchronous Binary Counter with D Flip-Flops
3-bit Synchronous Binary Counter with D Flip-Flops
To derive the D flip-flop input from the state table
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ DC DB DA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0 0 0 0
Q+ = D

## Slide 30: 12.3 Design of Binary Counters
The D input equations derived from the maps are
Karnaugh Maps for D Flip-Flops

## Slide 31: 12.3 Design of Binary Counters
3-bit Synchronous Binary Counter with D Flip-Flops

## Slide 32: 12.3 Design of Binary Counters
State Graph
When U = 1, Up counting
When D = 1, Down counting
3-bit Synchronous Binary Up-Down Counter
State Table
CBA | C+B+A+ | 
 | U | D
000 | 001 | 111
001 | 010 | 000
010 | 011 | 001
011 | 100 | 010
100 | 101 | 011
101 | 110 | 100
110 | 111 | 101
111 | 000 | 110

## Slide 33: 12.3 Design of Binary Counters
3-bit Synchronous Binary Up-Down Counter Using D flip-flops
State Table
Logic Equations
CBA | C+B+A+ | 
 | U | D
000 | 001 | 111
001 | 010 | 000
010 | 011 | 001
011 | 100 | 010
100 | 101 | 011
101 | 110 | 100
110 | 111 | 101
111 | 000 | 110

## Slide 34: 12.3 Design of Binary Counters
3-bit Synchronous Binary Up-Down Counter Using D flip-flops
Logic Equations

## Slide 35: 12.3 Design of Binary Counters
Loadable Counter with Count Enable
Block Diagram
Function Table
(b)

## Slide 36: 12.3 Design of Binary Counters
Loadable Counter Using F/F, MUX, and gates
0
1
0
1
0
1

## Slide 37: 12.3 Design of Binary Counters
Next-state Equations for the Loadable Counter

## Slide 38: 12.4 Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops
State Graph for Counter
State Table
Present State C B A | Next State C+ B+ A+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 - - - 0 1 1 0 0 0 1 1 1 - - - - - - 0 1 0

## Slide 39: 12.4 Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops
Flip-Flop Inputs
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ TC TB TA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 1 0 0 - - - - - - 0 1 1 0 0 1 0 0 0 0 1 1 1 1 1 0 1 1 - - - - - - - - - - - - 0 1 0 1 0 1

## Slide 40: 12.4 Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops
Flip-Flop Input Functions
Present State C B A | Next State F/F Inputs C+ B+ A+ TC TB TA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 1 0 0 - - - - - - 0 1 1 0 0 1 0 0 0 0 1 1 1 1 1 0 1 1 - - - - - - - - - - - - 0 1 0 1 0 1

## Slide 41: 12.4 Counters for Other Sequences
The Other Method to Derive Input Functions from the Next-State Maps
Q Q+ | T
0 0 0 1 1 0 1 1 | 0 1 1 0
If Q = 0, then T = Q+
If Q = 1, then T = (Q+ )’
Input Function of T Flip-Flop

## Slide 42: 12.4 Counters for Other Sequences
Present State C B A | Next State C+ B+ A+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 - - - 0 1 1 0 0 0 1 1 1 - - - - - - 0 1 0
The Other Method to Derive Input Functions from the Next-State Maps
Q Q+ | T
0 0 0 1 1 0 1 1 | 0 1 1 0

## Slide 43: 12.4 Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops

## Slide 44: 12.4 Counters for Other Sequences
Timing Diagram for Non-Straight Binary Counter Using T Flip-Flops

## Slide 45: 12.4 Counters for Other Sequences
CBA = 001, 101, 110
Analysis for Unused States

## Slide 46: 12.4 Counters for Other Sequences
Analysis for Unused States
CBA = 001, 101, 110
110
101

## Slide 47: 12.4 Counters for Other Sequences
Design Procedure for a Counter Using T Flip-Flop
Form a state table.
  Next states for each present states
2. Plot the next-state maps from the table.
3. Plot a T input map for each F/F .
4. Find the T input equations from the maps
5. Realize the circuit.

## Slide 48: 12.4 Counters for Other Sequences
Design of Non-Straight Binary Counter Using D Flip-Flop
Flip-Flop Input Function for D Flip-Flop: Q+ = D

## Slide 49: 12.4 Counters for Other Sequences
Design of Non-Straight Binary Counter Using D Flip-Flop

## Slide 50: 12.5 Counter Design Using S-R and J-K Flip-Flops
S-R Flip-Flop Inputs
Inputs not allowed
(a)
(b)
(c)

## Slide 51: 12.5 Counter Design Using S-R and J-K Flip-Flops
Design of Non-Straight Binary Counter Using S-R Flip-Flop

## Slide 52: 12.5 Counter Design Using S-R and J-K Flip-Flops
Design of Non-Straight Binary Counter Using S-R Flip-Flop

## Slide 53: 12.5 Counter Design Using S-R and J-K Flip-Flops
Design of Non-Straight Binary Counter Using S-R Flip-Flop

## Slide 54: 12.5 Counter Design Using S-R and J-K Flip-Flops
(a)
(b)
(c)
J-K Flip-Flop Inputs

## Slide 55: 12.5 Counter Design Using S-R and J-K Flip-Flops
Design of Non-Straight Binary Counter Using J-K Flip-Flop

## Slide 56: 12.6 Derivation of Flip-Flop Input Equations-Summary
Design of Non-Straight Binary Counter Using J-K Flip-Flop

## Slide 57: 12.6 Derivation of Flip-Flop Input Equations-Summary
Design of Non-Straight Binary Counter Using J-K Flip-Flop

## Slide 58: 12.6 Derivation of Flip-Flop Input Equations-Summary
Determination of Flip-Flop Input Equations from Next-State Equations Using Karnaugh Maps

## Slide 59: 12.6 Derivation of Flip-Flop Input Equations-Summary
Example (illustrating the use of Table 12-9)

## Slide 60: 12.6 Derivation of Flip-Flop Input Equations-Summary
Derivation of Flip-Flop Input Equations Using 4-Variable Maps