## Slide 1
UNIT 15 REDUCTION OF STATE TABLES STATE ASSIGNMENT
Objectives
Study Guide
15.1 Elimination of Redundant States
15.2 Equivalent States
15.3 Determination of State Equivalence Using an
Implication Table
15.4 Equivalent Sequential Circuits
15.5 Incompletely Specified State Tables
15.6 Derivation of Flip-Flop Input Equations
15.7 Equivalent State Assignments
15.8 Guidelines for State Assignment
15.9 Using a One-Hot State Assignment Problems

## Slide 2: Objectives
Define equivalent states, state several ways of testing for state
equivalence, and determine if two states are equivalent.
2. Define equivalent sequential circuits and determine if two circuits
are equivalent.
3. Reduce a state table to a minimum number of rows.
4. Specify a suitable set of state assignments for a state table,
eliminating those assignments which are equivalent with respect to
the cost of realizing the circuit
5. State three guidelines which are useful in making state assignments,
and apply these to making a good state assignment for a given
state table
6. Given a state table and assignment, form the transition table and
derive flip-flop input equations
7. Make a one-hot state assignment for a state graph and write the
next state and output equations by inspection.

## Slide 3
Example 1: Z=1 when input sequence 0101 or 1001 occurs.
The circuit resets after every four inputs.
Mealy Circuit
X = | 0101 | 0010 | 1001 | 0100
Z = | 0001 | 0000 | 0001 | 0000
A typical sequence of input and output
15.1 Elimination of Redundant States

## Slide 4: 15.1 Elimination of Redundant States
Partial State Graph for Example 1
state | sequence received
S0 S1 S2 S3 S4 | reset 0 1 01 or 10 010 or 100

## Slide 5: 15.1 Elimination of Redundant States
Complete State Graph for Example 1
state | sequence received
S0 S1 S2 S3 S4 S5 S6 | Reset 0 1 01 or 10 010 or 100 two inputs received, no 1 output is possible three inputs received, no 1 output is possible

## Slide 6: 15.1 Elimination of Redundant States
Table 15-1. State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | I | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
001 | I | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0

## Slide 7: 15.1 Elimination of Redundant States
Table 15-1. State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | I | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
001 | I | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
Same N.S. & Outputs
for the same inputs
H ≡ I

## Slide 8: 15.1 Elimination of Redundant States
Table 15-1. State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | I | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
001 | I | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
H ≡ I
Replace I with H
H

## Slide 9: 15.1 Elimination of Redundant States
Table 15-1. State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | H | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
Remove I

## Slide 10: 15.1 Elimination of Redundant States
Table 15-1. State Table for Sequence Detector (0101, 1001)
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | K | 0 | 0
F | L | M | 0 | 0
G | N | P | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
K | A | A | 0 | 0
L | A | A | 0 | 1
M | A | A | 0 | 0
N | A | A | 0 | 0
P | A | A | 0 | 0
H ≡ K, M, N, P
Replace K, M, N, P with H

## Slide 11: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | K H | 0 | 0
F | L | M H | 0 | 0
G | N H | P H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
K | A | A | 0 | 0
L | A | A | 0 | 1
M | A | A | 0 | 0
N | A | A | 0 | 0
P | A | A | 0 | 0
Table 15-2. State Table for Sequence Detector
H ≡ K, M, N, P
Replace K, M, N, P with H

## Slide 12: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | L | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
L | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
Remove K, M, N, P

## Slide 13: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | L | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
L | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
J ≡ L
Replace L with J

## Slide 14: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | L J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
L | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
J ≡ L
Replace L with J

## Slide 15: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
Remove L

## Slide 16: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
D ≡ G
Replace G with D

## Slide 17: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
D ≡ G
Replace G with D

## Slide 18: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
E ≡ F
Replace F with E

## Slide 19: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F E | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector
E ≡ F
Replace F with E

## Slide 20: 15.1 Elimination of Redundant States
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | E | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Table 15-2. State Table for Sequence Detector (Reduced)

## Slide 21: 15.1 Elimination of Redundant States
Fig 15-1. Reduced State Table and Graph for Sequence Detector
P.S. | N.S. |  | Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | E | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Row Matching
- Finding equivalent states
0

## Slide 22: 15.2 Equivalent States
Definition 15.1
Let N1 and N2 be sequential circuits (not necessarily different). Let X represent a sequence of inputs of arbitrary length. Then state p in N1 is equivalent to state q in N2 iff for every possible input sequence X.
are output sequences.

## Slide 23: 15.2 Equivalent States
Theorem 15.1
Two states p and q of a sequential circuit are equivalent iff for every single input X, the outputs are the same and the next states are equivalent, that is,
Equivalent
are output sequences.
are next state sequences.

## Slide 24: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | a-d c-e | a-f e-h |  |  |  |  | 
e |  |  | c-e a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g

## Slide 25: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | a-d c-e | a-f e-h |  |  |  |  | 
e |  |  | c-e a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove Self-implied

## Slide 26: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
After removing Self-implied

## Slide 27: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 28: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 29: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 30: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 31: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 32: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 33: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 34: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
After first pass

## Slide 35: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 36: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 37: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs

## Slide 38: 15.3 Determination of State Equivalence Using an Implication Table
Table 15-3.
Fig 15-3. Implication Chart for Table 15-3
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
After second pass

## Slide 39: 15.3 Implication Chart After First Pass
Fig 15-5. Implication Chart After Second Pass
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e c | d | 1
d | a | e c | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
Replace e with c

## Slide 40: 15.3 Implication Chart After First Pass
Fig 15-5. Implication Chart After Second Pass
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d a | c | 0
b | f | h | 0
c | c | d a | 1
d | a | c | 0
f | f | b | 1
g | b | h | 0
h | c | g | 1
Replace d with a

## Slide 41: 15.3 Implication Chart After First Pass
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | a | c | 0
b | f | h | 0
c | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
State table after reduction
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
State table before reduction

## Slide 42: 15.4 Equivalent Sequential Circuits
Definition 15.2
Sequential circuit N1 is equivalent to sequential circuit N2 if for each state p in N1 , there is a state q in N2 such that , and conversely, for each state s in N2 , there is a state t in N1 such that

## Slide 43: 15.4 Equivalent Sequential Circuits
Fig 15-6. Tables and Graphs for Equivalent Circuits
 | X=0 | X=1 | X=0 | X=1
A | B | A | 0 | 0
B | C | D | 0 | 1
C | A | C | 0 | 1
D | C | B | 0 | 0
 | X=0 | X=1 | X=0 | X=1
S0 | S3 | S1 | 0 | 1
S1 | S3 | S0 | 0 | 0
S2 | S0 | S2 | 0 | 0
S3 | S2 | S3 | 0 | 1

## Slide 44: 15.4 Equivalent Sequential Circuits
Fig 15-7. Implication Tables for Determining Circuit Equivalence

## Slide 45: 15.5 Incompletely Specified State Tables
Fig 15-8.
 | t0 | t1 | t2 |  | t0 | t1 | t2
X= | 1 | 0 | 0 | Z= | - | - | 0
 | 1 | 1 | 0 |  | - | - | 1
(- is a don’t care output)
The possible input-output sequence for circuit B
Table 15-5. Incompletely Specified State Table
 | X=0 X=1 |  | 0 1 | 
S0 | - | S1 | - | -
S1 | S2 | S3 | - | -
S2 | S0 | - | 0 | -
S3 | S0 | - | 1 | -
 | X=0 X=1 |  | 0 1 | 
S0 | (S0) | S1 | (0) | -
S1 | S2 S0 | S3 | (1) | -
S2 | S0 | (S1) | 0 | -
S3 | S0 | (S3) | 1 | -
 | X=0 X=1 |  | 0 1 | 
S0 | S0 | S1 | 0 | -
S1 | S0 | S1 | 1 | -

## Slide 46: 15.6 Derivation of Flip-Flop Input Equations
The procedure to drive the flip-flop input equations:
Assign flip-flop state values to correspond to the states in the reduced table
Construct a transition table which gives the next states of the flip-flops as a function of the present states and inputs
Derive the next-state maps from the transition table
Find flip-flop input maps from the next-state maps using the techniques developed in Unit 12 and find the flip-flop input equations from maps

## Slide 47: 15.6 Derivation of Flip-Flop Input Equations
Table 15-6
 | X=0 X=1 |  | 0 1 | 
S0 | S1 | S2 | 0 | 0
S1 | S3 | S2 | 0 | 0
S2 | S1 | S4 | 0 | 0
S3 | S5 | S2 | 0 | 0
S4 | S1 | S6 | 0 | 0
S5 | S5 | S2 | 1 | 0
S6 | S1 | S6 | 0 | 1
ABC | A+B+C+ |  | Z | 
 | X=0 | X=1 | 0 | 1
000 | 110 | 001 | 0 | 0
110 | 111 | 001 | 0 | 0
001 | 110 | 011 | 0 | 0
111 | 101 | 001 | 0 | 0
011 | 110 | 010 | 0 | 0
101 | 101 | 001 | 1 | 0
010 | 110 | 010 | 0 | 1

## Slide 48: 15.6 Derivation of Flip-Flop Input Equations
Fig. 15-9 Next-State Maps for Table 15-6

## Slide 49: 15.6 Derivation of Flip-Flop Input Equations
Table 15-7
PS | Next State |  |  |  | Output(Z1Z2) |  |  | 
 | X1X2= |  |  |  | X1X2= |  |  | 
 | 00 | 01 | 11 | 10 | 00 | 01 | 11 | 10
S0 | S0 | S0 | S1 | S1 | 00 | 00 | 01 | 01
S1 | S1 | S3 | S2 | S1 | 00 | 10 | 10 | 00
S2 | S3 | S3 | S2 | S2 | 11 | 11 | 00 | 00
S3 | S0 | S3 | S2 | S0 | 00 | 00 | 00 | 00
AB | A+B+ |  |  |  | Output(Z1Z2) |  |  | 
 | X1X2= |  |  |  | X1X2= |  |  | 
 | 00 | 01 | 11 | 10 | 00 | 01 | 11 | 10
00 | 00 | 00 | 01 | 01 | 00 | 00 | 01 | 01
01 | 01 | 10 | 11 | 01 | 00 | 10 | 10 | 00
11 | 10 | 10 | 11 | 11 | 11 | 11 | 00 | 00
10 | 00 | 10 | 11 | 00 | 00 | 00 | 00 | 00
(a) State table
(b) Transition table

## Slide 50: 15.6 Derivation of Flip-Flop Input Equations
Fig.15-10 Next-State Maps for Table 15-7
Fig.15-11 Derivation of S-R Equations for Table 15-7

## Slide 51: 15.7 Equivalent State Assignments
Table 15-8. State Assignments for 3-Row Tables
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  | 19 | 20 | 21 | 22 | 23 | 24
S0 | 00 | 00 | 00 | 00 | 00 | 00 | 01 | … | 11 | 11 | 11 | 11 | 11 | 11
S1 | 01 | 01 | 10 | 10 | 11 | 11 | 00 |  | 00 | 00 | 01 | 01 | 10 | 10
S2 | 10 | 11 | 01 | 11 | 01 | 10 | 10 |  | 01 | 10 | 00 | 10 | 00 | 01
Fig. 15-12 Equivalent Circuits Obtained by Complementing Qk

## Slide 52: 15.7 Equivalent State Assignments
Fig. 15-13 Equivalent Circuits Obtained by Complementing Qk
Table 15-9
Assignments |  |  | Present State | Next State |  | Output | 
A3 | B3 | C3 |  | X=0 | 1 | 0 | 1
00 | 00 | 11 | S1 | S1 | S3 | 0 | 0
01 | 10 | 10 | S2 | S2 | S1 | 0 | 1
10 | 01 | 01 | S3 | S2 | S3 | 1 | 0

## Slide 53: 15.7 Equivalent State Assignments
The resulting J and K input equations
Table 15-10 Nonequivalent Assignments for Three and Four States
 | 3-State Assignments |  |  | 4-State Assignments |  | 
States | 1 | 2 | 3 | 1 | 2 | 3
a | 00 | 00 | 00 | 00 | 00 | 00
b | 01 | 01 | 11 | 01 | 01 | 11
c | 10 | 11 | 01 | 10 | 11 | 01
d | - | - | - | 11 | 10 | 10

## Slide 54: 15.7 Equivalent State Assignments
Table 15-11 Number of Distinct(Nonequivalent)State Assignments
Number of States | Minimum Number of State Variables | Number of Distinct Assignments
2 | 1 | 1
3 | 2 | 3
4 | 2 | 3
5 | 3 | 140
6 | 3 | 420
7 | 3 | 840
8 | 3 | 840
9 | 4 | 10,810,800
… | … | …
16 | 4 | 

## Slide 55: 15.8 Guidelines for State Assignment
Guidelines for state assignment
States which have the same next state for a given input should be given adjacent assignments
States which are the next states of the same state should be given adjacent assignments
States which have the same output for a given input should be given adjacent assignments

## Slide 56: 15.8 Guidelines for State Assignment
Fig. 15-14
ABC |  | X=0 | 1 | 0 | 1
000 | S0 | S1 | S2 | 0 | 0
110 | S1 | S3 | S2 | 0 | 0
001 | S2 | S1 | S4 | 0 | 0
111 | S3 | S5 | S2 | 0 | 0
011 | S4 | S1 | S6 | 0 | 0
101 | S5 | S5 | S2 | 1 | 0
010 | S6 | S1 | S6 | 0 | 1
(a) State table
The sets of adjacent states specified by Guidelines 1 and 2

## Slide 57: 15.8 Guidelines for State Assignment
Fig. 15-15 Next-State Maps for Figure 15-14

## Slide 58: 15.8 Guidelines for State Assignment
Fig. 15-16 State Table and Assignments
 | X=0 | 1 | X=0 | 1
a | a | c | 0 | 0
b | d | f | 0 | 1
c | c | a | 0 | 0
d | d | b | 0 | 1
e | b | f | 1 | 0
f | c | e | 1 | 0
(a)
The sets of adjacent states specified by each Guidelines

## Slide 59: 15.8 Guidelines for State Assignment
Table 15-12 Transition Table for Figure 15-16(a)
Q1Q2Q3 | Q1+ Q2+ Q3+ |  |  | 
 | X=0 | 1 | X=0 | 1
1 0 0 | 100 | 000 | 0 | 0
1 1 1 | 011 | 010 | 0 | 1
0 0 0 | 000 | 100 | 0 | 0
0 1 1 | 011 | 111 | 0 | 1
1 0 1 | 111 | 010 | 1 | 0
0 1 0 | 000 | 101 | 1 | 0

## Slide 60: 15.8 Guidelines for State Assignment
Fig. 15-17 Next-State and Output Maps for Table15-12
The D flip-flop input equations
The output equations

## Slide 61: 15.9 Using a One-Hot State Assignment
The One-hot assignment example
The next-state equation for Q3
Because Q0=1 implies Q1= Q2= Q3=0,
Fig. 15-18 Partial State Graph

## Slide 62: 15.9 Using a One-Hot State Assignment
The modified equations
The One-hot assignment example by replacing Q0 with Q’0
The next-state equations
The output equations