## Slide 1
UNIT 4 Applications of Boolean Algebra/ Minterm and Maxterm Expansions
Objectives
Study Guide
4.1 Conversion of English Sentences to Boolean
Equations
4.2 Combinational Logic Design Using a Truth Table
4.3 Minterm and Maxterm Expansions
4.4 General Minterm and Maxterm Expansions
4.5 Incompletely Specified Functions
4.6 Examples of Truth Table Construction
4.7 Design of Binary Adders and Subtracters

## Slide 2
Conversion of Verbal Description to Boolean Equations
Combinational Logic Design Using a Truth Table
Minterm and Maxterm Expansions
General Minterm and Maxterm Expansions
Incompletely Specified Functions (Don’t care term)
Examples of Truth Table Construction
Design of Binary Adders(Full adder) and Subtracters
Objective

## Slide 3: 4.1 Conversion of Verbal Description to Boolean Equations
Steps in designing a single-output combinational switching circuit
Find a switching function which specifies the desired behavior of the circuit
Find a simplified algebraic expression for the function
Realize the simplified function using available logic elements

## Slide 4: 4.1 Conversion of Verbal Description to Boolean Equations
Mary watches TV if it is Monday night and she has finished her homework.
F is ‘true’ if A and B are both ‘true’  F = A·B
Example
F = 1 if “Mary watches TV ” is true; otherwise, F = 0;
A = 1 if “it is Monday night ” is true; otherwise, A = 0;
B = 1 if “she has finished her homework” is true; otherwise, B = 0;

## Slide 5
4.1 Conversion of Verbal Description to Boolean Equations
1. Verbal Description
The alarm will ring iff the alarm switch is turned on and the door is not closed, or it is after 6PM and window is not closed.
The alarm will ring iff
the alarm switch is turned on and the door is not closed,
or it is after 6PM and window is not closed.
Z
A
B’
C
D’
Breaking Down

## Slide 6
4.1 Conversion of Verbal Description to Boolean Equations
2. Boolean Equation
The alarm will ring iff
the alarm switch is turned on and the door is not closed,
or it is after 6PM and window is not closed.
Z
A
B’
C
D’

## Slide 7
4.1 Conversion of Verbal Description to Boolean Equations
2. Boolean Equation
3. Circuit Realization

## Slide 8
4.2 Combinational Logic Design Using a Truth Table
A switching circuit with three inputs and one output
The inputs are A, B, and C and represent a binary number N
f = 1 if N ≥ 0112 and f = 0 if N < 0112
Verbal Description

## Slide 9
4.2 Combinational Logic Design Using a Truth Table
Deriving an algebraic expression for f = 1
Simplifying the algebraic expression

## Slide 10
Simplified Equation
Circuit Realization
Original Equation
4.2 Combinational Logic Design Using a Truth Table

## Slide 11
Expression for f = 0 i.e. f’ = 1
Taking the complement of f ’
4.2 Combinational Logic Design Using a Truth Table

## Slide 12
Expression for f = 0
4.2 Combinational Logic Design Using a Truth Table

## Slide 13
Simplifying
4.2 Combinational Logic Design Using a Truth Table

## Slide 14: 4.3 Minterm and Maxterm Expansions
Literal
A variable or its complement (e.g. A, A’)
Minterm of n variables
A product of n literals in which each variable appears exactly once in either true or complemented form, but not both
Notation
mi

## Slide 15: 4.3 Minterm and Maxterm Expansions
Row No. | A B C | Minterms | Maxterms
0 1 2 3 4 5 6 7 | 0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | A’B’C’ = m0 A’B’C = m1 A’BC’ = m2 A’BC = m3 AB’C’ = m4 AB’C = m5 ABC’ = m6 ABC = m7 | A+B+C = M0 A+B+C’ = M1 A+B’+C = M2 A+B’+C’ = M3 A’+B+C = M4 A’+B+C’ = M5 A’+B’+C = M6 A’+B’+C’ = M7
Minterm of 3 variables

## Slide 16
4.3 Minterm and Maxterm Expansions
Sum of minterms
Minterm expansion
Standard sum of products
Canonical sum of products

## Slide 17: 4.3 Minterm and Maxterm Expansions
Maxterm of n variables
A sum of n literals in which each variable appears exactly once in either true or complemented form, but not both
Notation
Mi

## Slide 18: 4.3 Minterm and Maxterm Expansions
Row No. | A B C | Minterms | Maxterms
0 1 2 3 4 5 6 7 | 0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | A’B’C’ = m0 A’B’C = m1 A’BC’ = m2 A’BC = m3 AB’C’ = m4 AB’C = m5 ABC’ = m6 ABC = m7 | A+B+C = M0 A+B+C’ = M1 A+B’+C = M2 A+B’+C’ = M3 A’+B+C = M4 A’+B+C’ = M5 A’+B’+C = M6 A’+B’+C’ = M7
Maxterm of 3 variables

## Slide 19
4.3 Minterm and Maxterm Expansions
Product of maxterms
Maxterm expansion
Standard product of sums
Canonical product of sums

## Slide 20
4.3 Minterm and Maxterm Expansions
Finding Complement

## Slide 21
4.3 Minterm and Maxterm Expansions
Minterm and Maxterm expansions are complement each other

## Slide 22
4.3 Minterm and Maxterm Expansions
Introducing Missing Variables
Find the minterm expansion of
Maxterm expansion

## Slide 23: 4.4 General Minterm and Maxterm Expansions
General truth table for 3 variables
ai is either ‘0’ or ‘1’
Minterm expansion for general function
ai =1, minterm mi is present
ai =0, minterm mi is not present

## Slide 24: 4.4 General Minterm and Maxterm Expansions
General truth table for 3 variables
ai is either ‘0’ or ‘1’
Maxterm expansion for general function
ai =1, ai + Mi =1 , Maxterm Mi is not present
ai =0, Maxterm is present

## Slide 25
All minterms which are not present in F are present in F’
4.4 General Minterm and Maxterm Expansions
Finding Complement

## Slide 26
4.4 General Minterm and Maxterm Expansions
Finding Complement
All maxterms which are not present in F are present in F’

## Slide 27
4.4 General Minterm and Maxterm Expansions
Generalizing Equations for n Variables

## Slide 28: 4.4 General Minterm and Maxterm Expansions
If i and j are different, mi mj = 0
Product of Boolean functions
f1 f2 contains only those minterms which are present in both f1 and f2.

## Slide 29: 4.4 General Minterm and Maxterm Expansions
Example
Product of Boolean functions

## Slide 30: Conversion between minterm and maxterm expansions of F and F’
 | Minterm Expansion of F | Maxterm Expansion of F | Minterm Expansion of F’ | Maxterm Expansion of F’
Minterm Expansion of F |  | Maxterm nos. are those nos. not on the minterm list for F | List minterms not present in F | Maxterm nos. are the same as minterm nos. of F
Maxterm Expansion of F | Minterm nos. are those nos. not on the maxterm list for F |  | Minterm nos. are the same as maxterm nos. of F | List maxterms not present in F
GIVEN FORM
DESIRED FORM

## Slide 31: Conversion between minterm and maxterm expansions of F and F’
 | Minterm Expansion of F | Maxterm Expansion of F | Minterm Expansion of F’ | Maxterm Expansion of F’
F= ∑m(3,4,5,6,7) |  | ∏M(0,1,2) | ∑m(0,1,2) | ∏M(3,4,5,6,7)
F=∏M(0,1,2) | ∑m(3,4,5,6,7) |  | ∑m(0,1,2) | ∏M(3,4,5,6,7)
GIVEN FORM
DESIRED FORM
For Three Variables

## Slide 32: 4.5 Incompletely Specified Functions
If N1 output does not generate all possible combination of A, B, C, the output of N2(F) has don’t care values.
Truth Table with Don’t Cares
Don’t Care

## Slide 33: 4.5 Incompletely Specified Functions
When realize, assign values which will help simplify the function
Case 1: assign ‘0’ on X’s
Case 2: assign ‘1’ to the first X and ‘0’ to the second ‘X’
Case 3: assign ‘1’ on X’s
The case 2 leads to the simplest function
Don’t Care

## Slide 34
4.5 Incompletely Specified Functions
Minterm expansion for incompletely specified function
Don’t Cares
Maxterm expansion for incompletely specified function
Notation for Don’t Care Terms
Don’t Cares

## Slide 35: 4.7 Design of Binary Adders and Subtracters
Truth Table for a Half Adder
Half Adder
Half
Adder
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 1
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 1

## Slide 36: 4.7 Design of Binary Adders and Subtracters
Truth Table for a Full Adder
Full Adder
Full
Adder
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1

## Slide 37: 4.7 Design of Binary Adders and Subtracters
Implementation of Full Adder

## Slide 38: 4.7 Design of Binary Adders and Subtracters
Parallel Adder for 4 bit Binary Numbers
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 

## Slide 39: 4.7 Design of Binary Adders and Subtracters
Parallel Adder Composed of Four Full Adders
Carry Ripple Adder (slow!)

## Slide 40
The end-around carry is accomplished by connecting C4 to C0 input
4.7 Design of Binary Adders and Subtracters
Signed numbers in 1’s complement
Signed numbers in 2’s complement
The last carry (C4) is discarded, and no carry into the first cell

## Slide 41
Overflow(V) when adding two signed binary number
4.7 Design of Binary Adders and Subtracters

## Slide 42
4.7 Design of Binary Adders and Subtracters
Binary Subtracter Using Full Adder
Subtraction is done by adding the 2’s complemented number to be subtracted
2’s complemented number

## Slide 43
Parallel Subtracter Using Full Subtracters
4.7 Design of Binary Adders and Subtracters
Full Subtracter
bn+1
dn
xn
yn
bn
Full Subtracter
di
xi
yi
bi+1
bi
Full Subtracter
Full Subtracter
d2
d1
x2
y2
x1
y1
b2
b1=0
b3

## Slide 44
Truth Table For Binary Full Subtracter
4.7 Design of Binary Adders and Subtracters
xi yi bi | Bi+1 di
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 1 1 1 1 0 0 1 0 1 0 0 1 1