## Slide 1
UNIT 5 KARNAUGH MAPS
Objectives
Study Guide
5.1 Minimum Forms of Switching Functions
5.2 Two- and Three-Variable Karnaugh Maps
5.3 Four-Variable Karnaugh Maps
5.4 Determination of Minimum Expressions
5.5 Five-Variable Karnaugh Maps
5.6 Other Uses of Karnaugh Maps
5.7 Other Forms of Karnaugh Maps
Programmed Exercises
Problems

## Slide 2: Objectives
Given a function (completely or in completely specified) of three to five variable, plot it on a Karnaugh map. The function may be given in minterm, maxterm, or algebraic form.
Determine the essential prime implicants of a function from a map.
Obtain the minimum sum-of-products or minimum product-of-sums form of a function from the map.
Determine all of the prime implicants of a function from a map.
Understand the relation between operations performed using the map and the corresponding algebraic operation.

## Slide 3: Karnaugh Maps
Difficult to apply in a systematic way.
Difficult to tell when you have arrived at a minimum solution.
Two Problems of Simplifying a Switching Function Using Algebraic Techniques
Karnaugh Map method and Quine-McCluskey Procdure
Easy and systematic to get a a minimum solution.

## Slide 4: 5.1 Minimum Forms of Switching Functions
Realizing a switching function using AND and OR gates
Sum-of-Products form

## Slide 5: 5.1 Minimum Forms of Switching Functions
Sum-of-Products form
What we want is a circuit with
Minimum number of gates
Minimum number of gate inputs
Minimum number of terms
Minimum number of literals
Minimum Sum-of-Products form

## Slide 6: 5.1 Minimum Forms of Switching Functions
Procedure for obtaining a minimum sum-of-products
Eliminate redundant terms by using the consensus theorem or other theorems.
Combine terms by using . Do this repeatedly to eliminates as many literals as possible.
A given term may be used more than once because

## Slide 7: 5.1 Minimum Forms of Switching Functions
The result may depend on the order in which terms are combined or eliminated
Example: Find a minimum sum-of-products

## Slide 8: 5.1 Minimum Forms of Switching Functions
Example: Find a minimum product-of-sums
Eliminated by consensus
dual

## Slide 9: 5.2 Two- and Three-Variable Karnaugh Maps
A 2-variable Karnaugh Map

## Slide 10: 5.2 Two- and Three-Variable Karnaugh Maps
A B | F
0 0 0 1 1 0 1 1 | 1 1 0 0
Example: Truth table and Karnaugh map for a two-variable function
(a)

## Slide 11: 5.2 Two- and Three-Variable Karnaugh Maps
A B C | F
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 1 1 0 1 0
(a)
Example: Truth table and Karnaugh map for a three-variable function

## Slide 12: 5.2 Two- and Three-Variable Karnaugh Maps
Location of minterms on a three-variable Karnaugh map
Minterms in adjacent squares differ in only one variable
Can be combined using the theorem

## Slide 13: 5.2 Two- and Three-Variable Karnaugh Maps
Karnaugh Map of
Plot of minterm: mark 1
Plot of maxterm: mark 0
Plot of minterms and maxterms

## Slide 14: 5.2 Two- and Three-Variable Karnaugh Maps
Karnaugh maps for non-minterm product terms
term b
term bc’
term ac’

## Slide 15: 5.2 Two- and Three-Variable Karnaugh Maps
Karnaugh maps for non-minterm product terms

## Slide 16: 5.2 Two- and Three-Variable Karnaugh Maps
Simplification of a Three-Variable Function

## Slide 17: 5.2 Two- and Three-Variable Karnaugh Maps
Complement of a function
F’:
Replace 0 → 1
and 1 → 0

## Slide 18: 5.2 Two- and Three-Variable Karnaugh Maps
Karnaugh map for consensus theorem
Consensus term is redundant

## Slide 19: 5.2 Two- and Three-Variable Karnaugh Maps
Function with two minimum forms

## Slide 20: 5.3 Four-Variable Karnaugh Maps
Location of minterms on four-variable Karnaugh map

## Slide 21: 5.3 Four-Variable Karnaugh Maps
Plot of a function

## Slide 22: 5.3 Four-Variable Karnaugh Maps
Simplification of four-variable function

## Slide 23: 5.3 Four-Variable Karnaugh Maps
Simplification of four-variable function

## Slide 24: 5.3 Four-Variable Karnaugh Maps
Simplification of an function with don’t care conditions
don’t care term

## Slide 25: 5.3 Four-Variable Karnaugh Maps
Find minimum product-of-sums by using Karnaugh map
Plot 1’s of f
Group 0’s in the map → f’
Apply DeMorgan’s law
Given

## Slide 26: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Implicants of F
  Any product term in sum-of products form
Prime Implicants of F
  A product term which can not be combined with other terms to eliminate variable
Prime Implicants
Non-Prime Implicants

## Slide 27: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Prime Implicants
Non-Prime Implicants
Determination of Prime Implicants (PI)
A single 1 on a map can be a PI if it is not adjacent to any other 1’s.
Two adjacent 1’s if they are not contained in a group of four 1’s.
Four adjacent 1’s if they are not contained in a group of eight 1’s.
And so on…

## Slide 28: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Prime Implicants and Minimum Solution
ab

## Slide 29: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Procedure for Selecting Prime Implicants
CD is chosen first
Other PI’s are chosen first

## Slide 30: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Essential Prime Implicants (EPI)
  If a minterm is covered by only one PI, the PI is said to be an EPI
m5
m14
m2
BD, B’C, AC: EPI

## Slide 31
5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Procedure for Selecting EPI
Loop all PI
Find minterm covered by only one PI
Select that PI as an EPI
Repeat step 2 and 3
1. m4 is covered by only BC’
2. m10 is covered by only AC
3. BC’ and AC are EPI
AB
CD
00
01
11
10
00
01
11
10
0
4
8
12
1
3
2
7
6
9
11
10
13
15
14
5
1
1
1
1
1
1
1
1
1
1
BC’
AC

## Slide 32: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Approach for Finding EPIs
If a given minterm and all of the 1’s adjacent to it are covered by a single term, then that term is an EPI.
If all of the 1’s adjacent to a given minterm are not covered by a single term, then there are two or more PIs which cover that minterm, and we cannot say whether these PIs are essential or not without checking other minterms.

## Slide 33: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Approach for Finding EPIs
AB
CD
00
01
11
10
00
01
11
10
0
4
8
12
1
3
2
7
6
9
11
10
13
15
14
5
1
1
1
1
1
1
1
1
Check adjacent 1’s for m0(10)
  No single term covers 10, 11, 12, 14.
  No EPIs
Check adjacent 1’s for 11
  A’C’ covers 11, 10, 15.
  A’C’ is an EPI.
A’C’
Check adjacent 1’s for 12
  A’B’D’ covers 12, 10.
  A’B’D’ is an EPI.
A’B’D’

## Slide 34: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Approach for Finding EPIs
Check adjacent 1’s for 17
  No single term covers 17, 15, 115.
  No EPIs
AB
CD
00
01
11
10
00
01
11
10
0
4
8
12
1
3
2
7
6
9
11
10
13
15
14
5
1
1
1
1
1
1
1
1
A’C’
A’B’D’
Check adjacent 1’s for 111
  ACD covers 11, 10, 15.
  ACD is an EPI.
ACD
A’BD
A’BD or BCD is selected to include 17.
BCD

## Slide 35: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
Flowchart for Determining a Minimum SOP Using a Karnaugh Map
Choose a 1 which has not been covered.
Find all adjacent 1’s and X’s.
Are the chosen 1 and its adjacent 1’s and X’s covered by a single term?
That term is an EPI. Loop it.
All uncovered 1’s checked?
Find a minimum set of prime implicants which cover the remaining 1’s on the map.
Stop.
YES
NO
YES
NO

## Slide 36: 5.4 Determination of Minimum Expressions Using Essential Prime Implicants
110
16
X15
X7
19
113
15
18
14
X0
AB
CD
00
01
11
10
00
01
11
10
A’B covers 16 and its adjacent  EPI
A’B
AB’D’ covers 110 and its adjacent  EPI
AB’D’
AC’D is chosen for minimal cover  AC’D is not an EPI
AC’D

## Slide 37: 5.5 Five-Variable Karnaugh Maps
Two Layers of Four-Variable Karnaugh Map

## Slide 38: 5.5 Five-Variable Karnaugh Maps
Five Adjacent Terms
Four adjacent terms in the same layer
One adjacent term in the other layer

## Slide 39: 5.5 Five-Variable Karnaugh Maps
Resulting minimum solution

## Slide 40: 5.5 Five-Variable Karnaugh Maps
Final solution

## Slide 41: 5.6 Other Uses of Karnaugh Maps
Finding Common Terms

## Slide 42: 5.6 Other Uses of Karnaugh Maps
A Guide for Simplifying a Function Algebraically
ACDE

## Slide 43: 5.7 Other Forms of Karnaugh Maps
Veitch Diagrams

## Slide 44: 5.7 Other Forms of Karnaugh Maps
Other Forms of Five-Variable Karnaugh Maps