## Slide 1
UNIT 6 QUINE-McCLUSKEY METHOD
Objectives
Study Guide
6.1 Determination of Prime Implicants
6.2 The Prime Implicant Chart
6.3 Petrick’s Method
6.4 Simplification of Incompletely Specified Functions
6.5 Simplification Using Map-Entered Variables
6.6 Conclusion
Programmed Exercises
Problems

## Slide 2
Objectives
Find the prime implicants of a function by using the
Quine-McCluskey method.
2. Define prime implicants and essential prime implicants
3. Given the prime implicants, find the essential prime implicants
and a minimum sum-of-products expression for a function, using
a prime implicant chart and using Petrick method
4. Minimize an incompletely specified function, using the
Quine-McCluskey method
5. Find a minimum sum-of-products expression for a function,
using the method of map-entered variables

## Slide 3
Quine-McCluskey Method
Used when the number of variables is large
Provides systematic simplification procedure which can be readily programmed for a digital computer.
Quine-McCluskey Method
Eliminate as many literals as possible from each term by systematically applying the theorem
XY + XY’ = X
The resulting terms are called prime implicants
Use a implicant chart to select a minimum set of prime implicants
Reduction Procedure

## Slide 4: 6.1 Determination of Prime Implicants
The minterms are represented in binary notation and combined using
if two terms differ in exactly one variable.
Convert the given function into a sum-of minterms form

## Slide 5: 6.1 Determination of Prime Implicants
Example 1
Two terms differ in two variables, so it cannot be combined.
The dash(-) indicates a missing variable
-
Example 2

## Slide 6
6.1 Determination of Prime Implicants
Given binary minterms are sorted into groups according to the number of 1’s in each term.
Example
group 0 | 0 | 0000
group 1 | 1 | 0001
 | 2 | 0010
 | 8 | 1000
group 2 | 5 | 0101
 | 6 | 0110
 | 9 | 1001
 | 10 | 1010
group 3 | 7 | 0111
 | 14 | 1110

## Slide 7: 6.1 Determination of Prime Implicants
group 0 | 0 | 0000 | √
group 1 | 1 2 8 | 0001 0010 1000 | √ √ √
group 2 | 5 6 9 10 | 0101 0110 1001 1010 | √ √ √ √
group 3 | 7 14 | 0111 1110 | √ √
0, 1 | 000- | √
0, 2 | 00-0 | √
0, 8 | -000 | √
1, 5 | 0-01 | 
1, 9 | -001 | √
2, 6 | 0-10 | √
2,10 | -010 | √
8, 9 | 100- | √
8,10 | 10-0 | √
5, 7 | 01-0 | 
6, 7 | 011- | 
6,14 | -110 | √
10,14 | 1-10 | √
Determination of Prime Implicants
0, 1, 8, 9 0, 2, 8,10 0, 8, 1, 9 0, 8, 2,10 | -00- -0-0 -00- -0-0
2, 6,10,14 2,10, 6,14 | --10 --10
Column I
Column II
Column III

## Slide 8: 6.1 Determination of Prime Implicants
The function is equal to the sum of its prime implicants
(1,5) (5,7) (6,7) (0,1,8,9) (0,2,8,10) (2,6,10,14)
Apply consensus theorem to eliminate redundant terms
Consensus theorem:
Minimum sum-of-products

## Slide 9: 6.1 Determination of Prime Implicants
Definition of Implicant
Given a function F of n variables, a product term P is an implicants of F iff for every combination of values of the n variables for which P=1, F is also equal to 1.
Emaxple
Every term in the equation is an implicant, but bc is not.

## Slide 10: 6.1 Determination of Prime Implicants
Definition of Implicant:
A Prime Implicants of a function F is a product term implicant which is no longer an implicant if any literal is deleted from it.
Emaxple
Implicant a’b’c’ is not a Prime Implicants because b’c’ is still an implicant.
b’c’ and ac are Prime Implicants.

## Slide 11: 6.2 The Prime Implicant Chart
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x | x |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | x
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x | x |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | x
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
Select Essential Prime Implicants

## Slide 12: 6.2 The Prime Implicant Chart
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
Select Essential Prime Implicants

## Slide 13: 6.2 The Prime Implicant Chart
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
Select Essential Prime Implicants

## Slide 14: 6.2 The Prime Implicant Chart
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) | √ |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) | √ |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
The resulting minimum sum of products is
Select Essential Prime Implicants

## Slide 15: 6.2 The Prime Implicant Chart
Example: cyclic prime implicants(two more X’s in every column in chart)
Derivation of prime implicants

## Slide 16: 6.2 The Prime Implicant Chart
The resulting prime implicant chart (Table 6-4)
①
②
③
One solution:
x
x
(6,7)
x
x
(5,7)
x
x
'
(2,6)
x
x
'
(1,5)
x
x
'
'
(0,2)
x
x
'
'
1)
(0,
7
6
5
2
1
0
ad
ac
bc
c
b
c
a
b
a
®
®
®

## Slide 17: 6.2 The Prime Implicant Chart
Again starting with the other prime implicant that covers column 0.
The resulting table (Table6-5)
Finish the solution and show that

## Slide 18: 6.3 Petrick’s Method
Because we must cover all of the minterms,
the following function must be true:
- A technique for determining all minimum SOP solution from a PI chart
minterm0
minterm1

## Slide 19
First, we multiply out, using (X+Y)(X+Z) = X+YZ and
the ordinary Distributive law
Use X+XY=X to eliminate redundant terms from P
- Reduce P to a minimum SOP
- Choose P1,P4,P5 or P2,P3,P6 for minimum solution
or
6.3 Petrick’s Method

## Slide 20: 6.4 Simplification of Incompletely Specified Functions
Example:
Don’t care terms are treated like required minterms…

## Slide 21: 6.4 Simplification of Incompletely Specified Functions
Don’t care columns are omitted when forming the PI chart…
Replace each term in the final expression for F
The don’t care terms in the original truth table for F

## Slide 22: 6.5 Simplification Using Map-Entered Variables
Using of Map-Entered Variables (Figure 6-1)
The map represents the 6-variable function

## Slide 23: 6.5 Simplification Using Map-Entered Variables
Use a 3-variable map to simplify the function:
Simplification Using a Map-Entered Variable (Figure 6-2)

## Slide 24: 6.5 Simplification Using Map-Entered Variables
From Figure 6-2(b),
Find a sum-of-products expression for F of the form
The resulting expression is a minimum sum of products for G(Fig. 6-1) :
MS0 : minimum sum obtained by P1=P2=…=0
MS1 : minimum sum obtained by P1=1, Pj=0(j=/ 1) and replacing
all ‘1’’s on the map with ‘don’t cares(X)’
MS2 :….