## Slide 1
UNIT 9 MULTIPLEXERS, DECODERS, AND PROGRAMMABLE LOGIC DEVICES
This chapter in the book includes:
Objectives
Study Guide
9.1 Introduction
9.2 Multiplexers
9.3 Three-State Buffers
9.4 Decoders and Encoders
9.5 Read-Only Memories
9.6 Programmable Logic Devices
9.7 Complex Programmable Logic Devices
9.8 Field Programmable Gate Arrays
Problems

## Slide 2: Objectives
Explain the function of a multiplexer and implement a multiplexer using gates.
Explain the operation of three-state buffers. Determine the resulting output when three-state buffers outputs are connected together. Use three-state buffers to multiplex signals onto a bus.
Explain the operation of a decoder and encoder and use a decoder with added gates to implement a set of logic functions. Implement a decoder or priority encoder using gates.
Explain the operation of a read-only memory (ROM) and use a ROM to implement a set of logic functions.
Explain the operation of a programmable logic array (PLA). Use a PLA to implement a set of logic functions. Given a PLA table or an internal connection diagram for a PLA, determine the logic functions realized.
Explain the operation of a programmable array logic device (PAL). Determine the programming pattern required to realize a set of logic function with a PAL.
Explain the operation of a complex programmable logic device (CPLD) and a field programmable gate array (FPGA).
Use Shannon’s expansion theorem to decompose a switching function.

## Slide 3: 9.1 Introduction
IC (Integrated Circuit)
  SSI (Small-Scale Integration)
  MSI (Medium-Scale Integration)
  LSI (Large-Scale Integration)
  VLSI (Very-Large-Scale Integration)
Multiplexers
Three-state Buffer
Decoders and Encoders
ROMs
PLD
PLA
CPLD
FPGA

## Slide 4: 9.2 Multiplexers
2-to-1 Multiplexer and Switch Analog
Logic equation for the 2-to-1 MUX
Multiplexer (MUX, Data Selector)

## Slide 5: 9.2 Multiplexers
4-to-1 Multiplexer
Logic equation for the 4-to-1 MUX

## Slide 6: 9.2 Multiplexers
8-to-1 Multiplexer
Logic equation for the 8-to-1 MUX

## Slide 7: 9.2 Multiplexers
2n-to-1 Multiplexer
Logic equation for the 2 n - to - 1 MUX
mk : minterm of the n control variables
Ik : corresponding data input

## Slide 8: 9.2 Multiplexers
Logic Diagram for 8-to-1 MUX

## Slide 9: 9.2 Multiplexers
Quadruple 2-to-1 Multiplexer Used to Select Data

## Slide 10: 9.2 Multiplexers
Quad Multiplexer with Bus Inputs and Output
X, Y : Bus input
Z : Bus output

## Slide 11: 9.3 Three-State Buffers
Gate Circuit with Added Buffer
The logic of the buffer input and output are the same (F = C)
Buffer is used to increase driving capability

## Slide 12: 9.3 Three-State Buffers
Three-State Buffer
The output is enabled when B = 1, disabled when B = 0
Tri-State Buffer
High-impedance (Hi-Z) state

## Slide 13: 9.3 Three-State Buffers
Four Kinds of Three-State Buffers
B A | C
0 0 0 1 1 0 1 1 | Z Z 0 1
(a)
B A | C
0 0 0 1 1 0 1 1 | Z Z 1 0
(b)
B A | C
0 0 0 1 1 0 1 1 | 0 1 Z Z
(c)
B A | C
0 0 0 1 1 0 1 1 | 1 0 Z Z
(d)

## Slide 14: 9.3 Three-State Buffers
Data Selection Using Three-State Buffers

## Slide 15: 9.3 Three-State Buffers
Circuit with Two Three-State Buffers
S1 | X | S2 0 | 1 | Z
X 0 1 Z | X X X X | X 0 X 0 | X X 1 1 | X 0 1 Z
X = Unknown
S1
S2

## Slide 16: 9.3 Three-State Buffers
4-Bit Adder with Four Sources for One Operand
Four Sources

## Slide 17: 9.3 Three-State Buffers
Integrated Circuit with Bi-Directional Input/Output Pin

## Slide 18: 9.4 Decoders and Encoders
3-to-8 Line Decoder
a b c | y0 | y1 | y2 | y3 | y4 | y5 | y6 | y7
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 0 0 0 0 0 | 0 1 0 0 0 0 0 0 | 0 0 1 0 0 0 0 0 | 0 0 0 1 0 0 0 0 | 0 0 0 0 10 0 0 | 0 0 0 0 0 10 0 | 0 0 0 0 0 0 10 | 0 0 0 0 0 0 0 1

## Slide 19: 9.4 Decoders and Encoders
A 4-to-10 Line Decoder

## Slide 20: 9.4 Decoders and Encoders
A 4-to-10 Line Decoder
BCD Input | Decimal Output |  |  |  |  |  |  |  |  | 
A B C D | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 0 0 0 0 0 0 1 0 0 1 0 0 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 0 1 1 1 1 0 0 0 1 0 0 1 1 0 1 0 1 0 1 1 1 1 0 0 1 1 0 1 1 1 1 0 1 1 1 1 | 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 | 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 | 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 | 1 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 | 1 1 1 1 0 1 1 1 1 1 1 1 1 1 1 1 | 1 1 1 1 1 0 1 1 1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 0 1 1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 0 1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 0 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 1 0 1 1 1 1 11
(c) Truth Table

## Slide 21: 9.4 Decoders and Encoders
Realization of a Multiple-Output Circuit Using a Decoder

## Slide 22: 9.4 Decoders and Encoders
8-to-3 Priority Encoder
y0 | y1 | y2 | y3 | y4 | y5 | y6 | y7 | a | b | c | d
0 1 X X X X X X X | 0 0 1 X X X X X X | 0 0 0 1 X X X X X | 0 0 0 0 1 X X X X | 0 0 0 0 01 X X X | 0 0 0 0 0 0 1 X X | 0 0 0 0 0 0 0 1 X | 0 0 0 0 0 0 0 0 1 | 0 0 0 0 0 1 1 1 1 | 0 0 0 1 1 0 0 1 1 | 0 0 1 0 1 0 1 0 1 | 0 1 1 1 1 1 1 1 1

## Slide 23: 9.5 Read-Only Memories
An 8-Word x 4-Bit ROM
A | B | C |  |  | F0 | F1 | F2 | F3
0 0 0 0 1 1 1 1 | 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 |  |  | 1 1 0 0 1 0 1 0 | 0 0 1 1 1 0 1 1 | 1 1 1 0 0 0 1 0 | 0 0 1 1 0 1 1 1
(a) Block diagram
(b) Truth table for ROM
typical data stored in ROM
(23 words of
4bits each)

## Slide 24: 9.5 Read-Only Memories
Read-Only Memory with n Inputs and m Outputs
n input Variables |  |  |  | m output Variables |  |  | 
00 00 00 00 11 11 11 11 | · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · | 00 01 10 11 00 01 10 11 |  |  | 100 010 101 110 001 110 011 111 | · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · · | 110 111 101 010 · · 011 110 000 101
typical data array stored
in ROM
(2n words of
m bits each)

## Slide 25: 9.5 Read-Only Memories
Basic ROM Structure

## Slide 26: 9.5 Read-Only Memories
An 8-Word x 4-Bit ROM

## Slide 27: 9.5 Read-Only Memories
Equivalent OR Gate for F0

## Slide 28: 9.5 Read-Only Memories
Hexadecimal to ASCII Code Converter
Input |  |  |  | Hex Digit |  |  | ASCII Code for Hex Digit |  |  |  |  |  | 
W | X | Y | Z |  |  |  | A6 | A5 | A4 | A3 | A2 | A1 | A0
0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 | 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1 | 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 |  | 0 1 2 3 4 5 6 7 8 9 A B C D E F |  | 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0 1 1 0 0 0 0 0 0 | 0 0 0 0 1 1 1 1 0 0 0 0 0 1 1 1 | 0 0 1 1 0 0 1 1 0 0 0 1 1 0 0 1 | 0 1 0 1 0 1 0 1 0 1 1 0 1 0 1 0

## Slide 29: 9.5 Read-Only Memories
ROM Realization of Code Converter

## Slide 30: 9.5 Read-Only Memories
Types of ROMs
Mask-programmable ROM
Programmable ROM
Electrically Erasable Programmable ROM

## Slide 31: 9.6 Programmable Logic Devices
Programmable Logic Array (PLA) Structure
Both AND array and OR array are programmable.

## Slide 32: 9.6 Programmable Logic Devices
PLA with Three Inputs, Five Product Terms, and Four Outputs

## Slide 33: 9.6 Programmable Logic Devices
AND-OR Array Equivalent to Figure 9-25

## Slide 34: 9.6 Programmable Logic Devices
PLA Table for Figure 9-25
Product Term |  | Inputs |  |  |  | Outputs |  |  | 
 |  | A | B | C |  | F0 | F1 | F2 | F3
A’B’ AC’ B BC’ AC |  | 0 1 - - 1 | 0 - 1 1 - | - 0 - 0 1 |  | 1 1 0 0 0 | 0 1 1 0 0 | 1 0 0 1 0 | 0 0 1 0 1

## Slide 35: 9.6 Programmable Logic Devices
PLA Realization of Equations (7-23b) (p194)
a | b | c | d |  | f1 | f2 | f3
0 1 1 - - - | 1 1 0 0 - 1 | - - 0 1 1 1 | 1 1 - - - - |  | 1 1 1 1 0 0 | 1 0 0 0 1 0 | 0 1 1 0 0 1
(a) PLA table

## Slide 36: 9.6 Programmable Logic Devices
Programmable Array Logic (PAL)
AND array is programmable and OR array is fixed.
PAL

## Slide 37: 9.6 Programmable Logic Devices
Programmable Array Logic (PAL)
logically equal
AND array is programmable and OR array is fixed.

## Slide 38: 9.6 Programmable Logic Devices
Connections to the AND gate inputs in a PAL is represented by X
Programmable Array Logic

## Slide 39: 9.6 Programmable Logic Devices
PAL Segment

## Slide 40: 9.6 Programmable Logic Devices
Implementation of a Full Adder Using a PAL

## Slide 41: 9.7 Complex Programmable Logic Devices
Basic Architecture of Xilinx XCR3064XL CPLD
4 Function Blocks: programmable AND-OR array
16 Macrocells per Block: flip-flop and MUXs

## Slide 42: 9.7 Complex Programmable Logic Devices
CPLD Function Block and Macrocell
(A Simplified Version of XCR3064XL)

## Slide 43: 9.8 Field Programmable Gate Arrays
Layout of a Typical FPGA

## Slide 44: 9.8 Field Programmable Gate Arrays
Simplified Configurable Logic Block (CLB)
Function Generator
Function Generator

## Slide 45: 9.8 Field Programmable Gate Arrays
Implementation of a Function Generator (Lookup Table, LUT)
a | b | c | d | f
0 0 · · 1 | 0 0 · · 1 | 0 0 · · 1 | 0 1 · · 1 | 0 1 · · 1

## Slide 46: 9.8 Field Programmable Gate Arrays
Decomposition if switching Functions

## Slide 47: 9.8 Field Programmable Gate Arrays
Decomposition if switching Functions

## Slide 48: 9.8 Field Programmable Gate Arrays
Function Expansion Using a Karnaugh Map

## Slide 49: 9.8 Field Programmable Gate Arrays
Realization of Five- and Six-Variable Functions
with Function Generators